## Slide 1
Devtools

## Slide 2: Unique Tool Support
Project
Manager
Built-in
Editor
Source Level
Debugger
MPASM
Assembler
C Compilers
Languages
Programmers
MPLAB-SIM
Simulator
Simulators
Real-ICE
MPLAB-ICE
2000 & 4000
Emulators/ Debuggers
Third Party
Other tools
MPLINK
MPLIB
SIMICE
Hardware
Simulator
MPLAB
Integrated Development Environment
PICSTART
Plus
PICkit 2
PRO MATEII
PM3
MPLAB-ICD2
PICkit 2
Express

## Slide 3: Development Systems MPLAB-ICE
Universal in-circuit emulator for PIC® MCUs
Windows™ compatible
MPLAB compatible
Parallel port interface
Complete source-level debugging
Real-time in-circuit emulation of PIC MCUs
Low voltage emulation
Program memory emulation and memory mapping up to 64K words
Notes: Talk about how not all of these features are on all ice’s.
Talk about how the ice uses processor modules.

## Slide 4: Development Systems MPLAB-ICE (continued)
Break/trace/trigger on program address/data, internal register address/data, external inputs, or bus cycle type (mid-range, hi-end, golden gate only)
Real-time trace with up to 32K x 128 buffer
Time stamp trace
External trigger input and output for logic analyzer/scope interface
Complex breakpoints of up to four levels. Sequential events, AND/OR events, filtered trace, time between two events, and pass counts.

## Slide 5: MPLAB-ICE 2000
Host to Pod Cable
*Emulator Pod
*Processor
Module
Flex Circuit
Cable
*Device
Adapter
*SOIC
Transition
Socket
*Each component
ordered separately

## Slide 6: Development Systems PICMASTER®
Universal in-circuit emulator for PIC MCUs
Windows™- and MPLAB-compatible
Complete source-level debugging
ISA PC interface card
Unlimited break/trace/trigger points
External break including AND/OR with internal breaks
Multiple processor emulation

## Slide 7: Development Systems ICEPIC
Low cost in-circuit emulator for PIC MCUs
Developed by RF Solutions (U.K.)
Windows-compatible
Complete source-level debugging
EIA232 serial interface
Unlimited breakpoints

## Slide 8: Development Systems MPLAB-SIM
Universal simulator for PIC MCUs
Windows and MPLAB-compatible
Discrete event instruction-based simulation
Complete source-level debugging
Support interrupts and most peripheral functions (not A/D or serial I/O)
Stimulus injection and file input capability
Free

## Slide 9: Development Systems MPLAB-ICD 2
Features
      USB (Full Speed 2 M bits/s) & RS-232 interface to host PC
      Real time background debugging
      MPLAB IDE GUI (free copy included)
      Built in over-voltage/short circuit monitor
      Firmware upgradeable from PC
      Totally enclosed
      Supports low voltage to 2.0 volts. (2.0 to 6.0 range)

## Slide 10: Development Systems MPLAB-ICD 2
Features Continued
      Diagnostic LEDs (Power, Busy, Error)
      Reading/Writing memory space and EEDATA areas of target microcontroller
      Programs configuration bits
      Erase of program memory space with verification
      Peripheral freeze-on-halt stops timers at breakpoints

## Slide 11: Development Systems MPLAB-ICD 2
There is some shared overhead expense that includes:
      one stack level,
      some general purpose file registers
      a small area of program memory when in the debug mode

## Slide 12: Development Systems PICSTART Plus
Development programmer kit
Supports all PIC MCUs
Windows- and MPLAB-compatible
CD-ROM literature

## Slide 13: Development Systems PICSTART Plus Development Programmer
Upgrades done in MPLAB software - firmware upgrades occasionally required for new PIC sub-families
Uses serial programming algorithms for all ICSP capable devices
PICSTART Plus
DEVELOPMENT PROGRAMMER
POWER
ACTIVE
RS-232 Serial
Interface
9V DC Input
Power ON
Programmer
Active
40-Pin ZIF Socket to accommodate PICs from 8- to 40-pins. 68-pin PLCC can be programmed with an adapter
Pin-1

## Slide 14: Development Systems PRO MATE® II
Universal device programmer for PIC MCUs
Stand-alone or PC DOS-compatible, MPLAB-compatible
EIA232 PC host interface
Interchangeable socket modules
Environment “save and restore”
Programmable voltages for verify
Serialized programming capabilities
ICSP support
Serial EEPROM support
KEELOQ® support

## Slide 15: Development Systems PICDEM-1, -2, -3, -14, -17
Demonstration board for PIC MCUs
On board +5V regulator
EIA232 interface
5K pot to simulate analog input
3 push buttons for external stimulus and reset
LED’s connected to PORTB
LCD display panel connection
Socket for crystal oscillator
Prototype area
Notes: -1 => 18 pin max
-2 => 40 pin max

## Slide 16
Development Systems PICDEM-1 Demo Board
Demo board
accommodates all 18-pin
PIC devices, 28-pin
PIC16C5X and 40-pin
PIC17C4X devices
8-LEDs connected to
PORTB
5k Pot connected to AN0
PB switches connected
to RA1, RTCC, and MCLR
LED
RS-232
Serial Interface
Crystal Oscillator
Socket
9V DC Input
Prototyping
Area
Potentiometer
on A/D Channel 0
RTCC
MCLR
RA1
RS-232 Level
Shifter (MAX-232)

## Slide 17: Development Systems MPASM
Universal macro assembler for all PIC MCUs
DOS- and Windows-compatible
Compatible with MPLAB
  Symbolic and source-level debugging
  Can generate relocatable code
Multiple output formats
Licensed by several third party vendors
Free

## Slide 18: Development Systems COMPILERS
Microchip MPLAB-C17
Microchip MPLAB-C18
Microchip MPLAB-C30
Hi-Tech
CCS
IAR
Byte Craft
Micro Engineering Labs (Basic)

## Slide 19: Development Systems Reference Materials
Application notes
  Embedded Controls Handbook
Reference designs
Website
  http://www.microchip.com
  Conference groups
  Mailing lists
Microchip CD ROM
Template subdirectory under MPLAB (code templates)
Seminars
Workshops

## Slide 20: Development Systems Third Party Guide
Microchip encourages third-party support
  312-page reference manual to aid in selection of appropriate tools
  106 companies and 208 products
    Emulators
    Programmers and gang programmers
    ‘C’ compilers, software, demo boards, etc.
  Design consultant reference

## Slide 21: Books For Further Research (English)
Design with PIC Microcontrollers, John Peatman, Prentice-Hall, 0-13-759259-0
Programming and Customizing the PIC Microcontroller, Myke Predko, McGraw-Hill, 0-07-913646-X
Easy PIC’n, David Benson, Square 1 Electronics, 0-9654162-0-8
PIC’n Up The Pace, David Benson, Square 1 Electronics, 0-9654162-1-6
A Beginners Guide to the Microchip PIC, Nigel Gardner, Bluebird Technical Press Ltd., 1-899013-01-6

## Slide 22: Books For Further Research (English)
PIC Cookbook Vol 1 & Vol 2, Nigel Gardner, Bluebird Technical Press Ltd., 1899013-02-4, 1-901631-00-1
The Greatest Little PIC Book, Gordon McNee, Bluebird Technical Press Ltd., 1-901631-01-X
PIC Microcontroller Operation and Applications, DN de Beer, Cape Technikon, daandb@norton.ctech.az.za
Getting started with PIC Microcontrollers, Al Stevens, Ziggurat Technologies, ziggurat@global.co.za

## Slide 23: Books For Further Research (French)
Les Microcontrolleurs PIC et mise en oeuvre, Christian Tavernier, Dunod, 2-10-002647-X
Micontrolleurs PIC a structure RISC, C.F. Urbain, Publitronic, 2-86661-058-X
Pratique des Microcontroleurs PIC, Francesco Volpe/Safinaz Volpe, Publitronic Elektor, 2-86661-077-6

## Slide 24: Books For Further Research (German)
Mit dem PIC-Controller Erfolgreich Arbeiten, Dr. Anne Koenig/Manfred Koenig, Markt & Technik Verlag, 3-8272-5168-0
Mikrokontroller mit RISC Struktur, C.F. Urbain, Elektor Compact, 3-928051-83-0
Mikroprozessor PIC16C5X, Michael Rose, Huthig, 3-7785-2169-1
Mikroprozessor PIC17C42, Michael Rose, Huthig, 3-7785-2170-5
PIC uC Praxis, Francesco Volpe/Safinaz Volpe, Elektor Verlag, 3-89576-030-7

## Slide 25: Books For Further Research (Italian/Russian/Spanish)
La Programmazione dei Microcontrollori PIC, Andrea Sbrana, Italy +39 544 464070
New Possibilities with the Microchip PIC, RIGA, Latvia +371 935 0550
MicroControladores PIC La Solution en un Chip, Martinez Usategui, Paraninfo,84-283-2371-2
MicroControladores PIC, Christian Tavernier, Paraninfo, 84-283-2373-9

## Slide 26: Books For Further Research (Chinese)
Parts 1-5 PIC16C5X/71/84 Development and Design, United Tech Electronic Co. Ltd,
  957-21-0807-7
  957-21-1152-3
  957-21-1187-6
  957-21-1251-1
  957-21-1257-0
PIC16C84 MCU Architecture and Software Development, ICC Company, 957-8716-79-6

## Slide 27: Microchip Technical Services Engineering Web Site
Web address: www.microchip.com
Latest versions available
  Datasheets
  User’s Guides
  Application Notes
  Device Errata
  Development tools
Frequently-Asked Questions (FAQs)
Latest product announcements
Recent press releases

## Slide 28: Microchip Technical Services
Workshops
  Hands on workshops using Microchip development tools
  Various topics in many cities
  Watch the web site for details
Address: www.microchip.com