## Slide 1: PIC MCUs
Instruction Set

## Slide 2: PIC MCU Instruction Set
33 instructions  12-bit core
35 instructions  14-bit core
58 instructions  16-bit core
  Easy to learn
  High compaction
  Very powerful single-word instructions
  All single-cycle except program branches
  Upward compatibility of instructions
Notes: Talk about the RISC and how since instruction set is small, code is portable to other parts.

## Slide 3: 12-bit Core Instruction Set: Instruction Set Summary
Byte-Oriented Operation
NOP - No Operation - 0000 0000 0000
MOVWF f Move W to f W  f 0000 001f ffff
CLRW - Clear W 0  W 0000 0100 0000
CLRF f,d Clear f 0  f 0000 011f ffff
SUBWF f,d Subtract W from f f - W  d[f+W+1  d] 0000 10df ffff
DECF f,d Decrement f f - 1  d 0000 11df ffff
IORWF f,d Inclusive OR W and f W v f  d 0001 00df ffff
ANDWF f,d AND W and f W & f  d 0001 01df ffff
XORWF f,d Exclusive OR W and f W  f  d 0001 10df ffff
ADDWF f,d Add W and f W + f  d 0001 11df ffff
MOVF f,d Move f f  d 0010 00df ffff
COMF f,d Complement f f  d 0010 01df ffff
INCF f,d Increment f f + 1  d 0010 10df ffff
DECFSZ f,d Decrement f, skip if zero f - 1  d, skip if zero 0011 11df ffff
RRF f,d Rotate right f f(n)  d(n-1), f(0)  C, C  d(7) 0011 00df ffff
RLF f,d Rotate left f f(n)  d(n+1), f(7)  C, C  d(0) 0011 01df ffff
SWAPF f,d Swap halves f f(0:3)  f(4:7)  d 0011 10df ffff
INCFSZ f,d Increment f, skip if zero f + 1  d, skip if zero 0011 11df ffff
Legends: f = file address <5>; b = bit address <3>; k = literal or immediate value (8 or 9 bit);
d = destination select; d = 0: W reg, d = 1: f

## Slide 4: 12-bit Core Instruction Set: Instruction Set Summary (Cont.)
Bit-Oriented Operations
BCF f,b Bit clear f 0 f(b) 0100 bbbf ffff
BSF f,b Bit set f 1 f(b) 0101 bbbf ffff
BTFSC f,b Bit test f, skip if clear Test bit (b) in file (f), skip if clear 0110 bbbf ffff
BTFSS f,b Bit test f, skip if set Test bit (b) in file (f), skip if set 0111 bbbf ffff
Literal and Control Operations
OPTION - Load OPTION register W  OPTION register 0000 0000 0010
SLEEP - Go into Standby Mode 0  WDT, stop oscillator 0000 0000 0010
CLRWDT - Clear Watchdog Timer 0  WDT 0000 0000 0100
TRIS f Tri-state™ Port f W  I/O control register f 0000 0000 0fff
RETLW k Return, place Literal in W k  W, Stack PC 1000 kkkk kkkk
CALL k Call Subroutine PC + 1 Stack, k PC 1001 kkkk kkkk
GOTO k Go to address (k is 9 bit) k PC (9 bits) 101k kkkk kkkk
MOVLW k Move Literal to W k W 1100 kkkk kkkk
IORLW k Inclusive OR Literal and W k v W W 1101 kkkk kkkk
ANDLW k AND Literal W k & W W 1110 kkkk kkkk
XORLW k Exclusive OR Literal W K  W W 1111 kkkk kkkk
Legends: f = file address <5>; b = bit address <3>; k = literal or immediate value (8 or 9 bit);
d = destination select; d = 0: W reg, d = 1: f

## Slide 5
PIC Instruction Set 14-bit core Summary
NOP - No Operation
MOVWF f Move W to f
CLRW - Clear W
CLRF f Clear f
SUBWF f,d Subtract W from f
DECF f,d Decrement f
IORWF f,d Inclusive OR W and f
ANDWF f,d AND W and f
XORWF f,d Exclusive OR W and f
ADDWF f,d Add W and f
MOVF f,d Move f
COMF f,d Complement f
INCF f,d Increment f
DECFSZ f,d Decrement f, skip if zero
RRF f,d Rotate right f through carry
RLF f,d Rotate left f through carry
SWAPF f,d Swap nibbles of f
INCFSZ f,d Increment f, skip if zero
BCF f,b Bit clear f
BSF f,b Bit set f
BTFSC f,b Bit test f, skip if clear
BTFSS f,b Bit test f, skip if set
SLEEP - Go into standby mode
CLRWDT - Clear watchdog timer
RETLW k Return, place literal in W
RETFIE - Return from interrupt
RETURN - Return from subroutine
CALL k Call subroutine
GOTO k Go to address (k is 9-bit)
MOVLW k Move literal to W
IORLW k Inclusive OR literal with W
ADDLW k Add literal with W
SUBLW k Subtract W from literal
ANDLW k AND literal with W
XORLW k Exclusive OR literal with W
Byte-Oriented Operations
Bit-Oriented Operations
Literal and Control Operations
f = File Register, k = literal value (8-bit), b = bit address <0,7>, d = destination (0=W, 1=f)

## Slide 6
PIC Instruction Set Byte-Oriented Operations
14-bit Instruction for Byte Oriented Operations
OP CODE
d
f
f
f
f
f
f
f
d = Destination Bit
d = 0 for destination W
d = 1 for destination f
f = 7-bit Register Address
Example:
ADDWF REG, W
ADDWF f, d
NOP -
MOVWF f
CLRW -
CLRF f
SUBWF f,d
DECF f,d
IORWF f,d
ANDWF f,d
XORWF f,d
ADDWF f,d
MOVF f,d
COMF f,d
INCF f,d
DECFSZ f,d
RRF f,d
RLF f,d
SWAPF f,d
INCFSZ f,d
Byte-Oriented
Operations

## Slide 7
PIC MCU Instruction Set Byte-Oriented Operations
NOP No Operation
Syntax: NOP
Operands: None
Operation: No operation
Status: None
Encoding: 00 0000 0000 0000
Words: 1
Cycles: 1
Example:
NOP

## Slide 8
PIC MCU Instruction Set Byte-Oriented Operations
MOVWF Move W to f
Syntax: MOVWF f
Operands: 0 <= f <= 127
Operation: (W) -> (f)
Status: None
Encoding: 00 0000 1fff fff
Words: 1
Cycles: 1
Example:
MOVWF FSR
Before Instruction
FSR = 0xFF
W = 0x4F
After Instruction
FSR = 0x4F
W = 0x4F

## Slide 9
PIC MCU Instruction Set Byte-Oriented Operations
CLRW Clear W
Syntax: CLRW
Operands: None
Operation: 00h -> (W)
1 -> Z
Status: Z
Encoding: 00 0001 0000 0000
Words: 1
Cycles: 1
Example:
CLRW
Before Instruction
W = 0x4F
After Instruction
W = 0x00
Z = 1

## Slide 10
PIC MCU Instruction Set Byte-Oriented Operations
CLRF Clear f
Syntax: CLRF f
Operands: 0 <= f <= 127
Operation: 00h -> (f)
1 -> Z
Status: Z
Encoding: 00 0001 1fff ffff
Words: 1
Cycles: 1
Example:
CLRF FSR
Before Instruction
FSR = 0x4F
After Instruction
FSR = 0x00
Z = 1

## Slide 11
PIC MCU Instruction Set Byte-Oriented Operations
SUBWF Subtract W from f
Syntax: SUBWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) - (W) -> dest
Status: C,DC,Z
Encoding: 00 0010 dfff ffff
Words: 1
Cycles: 1
Example:
SUBWF FSR,W
Before Instruction
FSR = 0x03
W = 0x02
C = ?
Z = ?
After Instruction
FSR = 0x03
W = 0x01
C = 0
Z = 0

## Slide 12
PIC MCU Instruction Set Byte-Oriented Operations
DECF Decrement f
Syntax: DECF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) - 1 -> dest
Status: Z
Encoding: 00 0011 dfff ffff
Words: 1
Cycles: 1
Example:
DECF FSR,F
Before Instruction
FSR = 0x01
Z = 0
After Instruction
FSR = 0x00
Z = 1

## Slide 13
PIC MCU Instruction Set Byte-Oriented Operations
IORWF Inclusive OR W & f
Syntax: IORWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W) .OR. (f) -> dest
Status: Z
Encoding: 00 0100 dfff ffff
Words: 1
Cycles: 1
Example:
IORWF CNT,W
Before Instruction
CNT = 0x13
W = 0x91
After Instruction
CNT = 0x13
W = 0x93
Z = 0

## Slide 14
PIC MCU Instruction Set Byte-Oriented Operations
ANDWF AND W with f
Syntax: ANDWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W).AND.(f) -> dest
Status: Z
Encoding: 00 0101 dfff ffff
Words: 1
Cycles: 1
Example:
ANDWF CNT,F
Before Instruction
CNT = B’00010111’
W = B’11000010’
After Instruction
CNT = B’00000010’
W = B’11000010’
Z = 0

## Slide 15
PIC MCU Instruction Set Byte-Oriented Operations
XORWF Exclusive OR W & f
Syntax: XORWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W).XOR.(f) -> dest
Status: Z
Encoding: 00 0110 dfff ffff
Words: 1
Cycles: 1
Example:
XORWF FSR,W
Before Instruction
FSR = B’10101111’
W = B’10110101’
After Instruction
FSR = B’10101111’
W = B’00011010’
Z = 0

## Slide 16
PIC MCU Instruction Set Byte-Oriented Operations
ADDWF Add W with f
Syntax: ADDWF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (W) + (f) -> dest
Status: Z
Encoding: 00 0111 dfff ffff
Words: 1
Cycles: 1
Example:
ADDWF FSR,W
Before Instruction
FSR = 0x17
W = 0xC2
After Instruction
FSR = 0x17
W = 0xD9
Z = 0

## Slide 17
PIC MCU Instruction Set Byte-Oriented Operations
MOVF Move f
Syntax: MOVF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) -> dest
Status: Z
Encoding: 00 1000 dfff ffff
Words: 1
Cycles: 1
Example:
MOVF FSR,F
Before Instruction
FSR = 0x00
Z = 0
After Instruction
FSR = 0x00
Z = 1

## Slide 18
PIC MCU Instruction Set Byte-Oriented Operations
COMF Complement f
Syntax: MOVF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) -> dest
Status: Z
Encoding: 00 1001 dfff ffff
Words: 1
Cycles: 1
Example:
COMF REG,W
Before Instruction
REG = 0x13
W = 0x58
Z = 0
After Instruction
REG = 0x13
W = 0xEC
Z = 0

## Slide 19
PIC MCU Instruction Set Byte-Oriented Operations
INCF Increment f
Syntax: INCF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) + 1 -> dest
Status: Z
Encoding: 00 1010 dfff ffff
Words: 1
Cycles: 1
Example:
INCF REG,F
Before Instruction
REG = 0xFF
Z = 0
After Instruction
REG = 0x00
Z = 1

## Slide 20
PIC MCU Instruction Set Byte-Oriented Operations
DECFSZ Dec. f, Skip if 0
Syntax: DECFSZ f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) - 1 -> dest
skip if result = 0
Status: None
Encoding: 00 1011 dfff ffff
Words: 1
Cycles: 1(2)
Example:
Loop DECFSZ CNT,F
GOTO Loop
Continue
Before Instruction
PC = address Loop
After Instruction
CNT = CNT - 1
if CNT = 0,
PC = address Continue
if CNT != 0,
PC = address Loop+1

## Slide 21
PIC MCU Instruction Set Byte-Oriented Operations
RRF Rotate Right f -> C
Syntax: RRF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation:
Status: C
Encoding: 00 1100 dfff ffff
Words: 1
Cycles: 1
Example:
RRF CNT,W
Before Instruction
CNT = 1110 0110
C = 0
After Instruction
CNT = 1110 0110
W = 0111 0011
C = 0
C
Register f

## Slide 22
PIC MCU Instruction Set Byte-Oriented Operations
RLF Rotate Left f -> C
Syntax: RLF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation:
Status: C
Encoding: 00 1101 dfff ffff
Words: 1
Cycles: 1
Example:
RLF CNT,W
Before Instruction
CNT = 1110 0110
C = 0
After Instruction
CNT = 1110 0110
W = 1100 1100
C = 1
C
Register f

## Slide 23
PIC MCU Instruction Set Byte-Oriented Operations
SWAPF Swap Nibbles in f
Syntax: SWAPF f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: f<3:0> -> dest<7:4>
f<7:4> -> dest<3:0>
Status: None
Encoding: 00 1110 dfff ffff
Words: 1
Cycles: 1
Example:
SWAPF REG,W
Before Instruction
REG = 0xA5
After Instruction
REG = 0xA5
W = 0x5A

## Slide 24
PIC MCU Instruction Set Byte-Oriented Operations
INCFSZ Inc. f, Skip if 0
Syntax: INCFSZ f,d
Operands: 0 <= f <= 127
d = {0,1}
Operation: (f) + 1 -> dest
skip if result = 0
Status: None
Encoding: 00 1111 dfff ffff
Words: 1
Cycles: 1(2)
Example:
Loop INCFSZ CNT,F
GOTO Loop
Continue
Before Instruction
PC = address Loop
After Instruction
CNT = CNT + 1
if CNT = 0,
PC = address Continue
if CNT != 0,
PC = address Loop+1

## Slide 25
PIC MCU Instruction Set Bit-Oriented Operations
14-bit Instruction for Bit Oriented Operations
OP CODE
b
f
f
f
f
f
f
f
b = 3-Bit Address
(Bit Number)
f = 7-bit Register Address
b
b
Example:
BTFSC STATUS, C
BTFSC f, b
BCF f,b
BSF f,b
BTFSC f,b
BTFSS f,b
Bit-Oriented
Operations

## Slide 26
PIC MCU Instruction Set Bit-Oriented Operations
BCF Bit Clear f
Syntax: BCF f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: 0 -> (f<b>)
Status: None
Encoding: 01 00bb bfff ffff
Words: 1
Cycles: 1
Example:
BCF FSR,4
Before Instruction
FSR = 0011 0000
After Instruction
FSR = 0010 0000

## Slide 27
PIC MCU Instruction Set Bit-Oriented Operations
BSF Bit Set f
Syntax: BSF f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: 1 -> (f<b>)
Status: None
Encoding: 01 01bb bfff ffff
Words: 1
Cycles: 1
Example:
BSF FSR,4
Before Instruction
FSR = 0010 0000
After Instruction
FSR = 0011 0000

## Slide 28
PIC MCU Instruction Set Bit-Oriented Operations
BTFSC Bit Test f, Skip if 0
Syntax: BTFSC f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: skip if (f<b>) = 0
Status: None
Encoding: 01 10bb bfff ffff
Words: 1
Cycles: 1(2)
Example:
Here BTFSC CNT,1
False GOTO Done
True
Before Instruction
PC = address Here
After Instruction
if CNT<1> = 0,
PC = address True
if CNT<1> = 1,
PC = address False

## Slide 29
PIC MCU Instruction Set Bit-Oriented Operations
BTFSS Bit Test f, Skip if 1
Syntax: BTFSS f,b
Operands: 0 <= f <= 127
0 <= b <= 7
Operation: skip if (f<b>) = 1
Status: None
Encoding: 01 11bb bfff ffff
Words: 1
Cycles: 1(2)
Example:
Here BTFSS CNT,1
False GOTO Done
True
Before Instruction
PC = address Here
After Instruction
if CNT<1> = 1,
PC = address True
if CNT<1> = 0,
PC = address False

## Slide 30: PIC MCU Instruction Set Example: Bit Manipulation
XMIT: MOVLW 0x08 ;Bit count = 8
MOVWF bit_count
XM_LOOP:
BCF PORTB,DT ;preset clock & data lines to 0
BCF PORTB,CLK ;preset clock & data lines to 0
RRF XDATA,F ;rotate data right thru Carry
BTFSC STATUS,C ;test carry bit
BSF PORTB,DT ;set 1  Data pin
BSF PORTB,CLK ;set 1  Clock pin
DECFSZ bit_count,F ;decrement count
GOTO XM_LOOP ;Not done then repeat
BCF PORTB,CLK ;clear clock line and exit
Synchronous serial transmission of eight bits of data from file register XDATA to I/O Pin:
Clock
Data
0
1
7

## Slide 31
PIC MCU Instruction Set Literal Operations
k
14-bit Instruction for Literal Operations
OP CODE
k
k
k
k
k
k
k
k = 8-bit Immediate Value
Example:
MOVLW 0x2F
MOVLW k
MOVLW k
IORLW k
ADDLW k
SUBLW k
ANDLW k
XORLW k
Literal
Operations

## Slide 32
PIC MCU Instruction Set Literal Operations
MOVLW Move Literal to W
Syntax: MOVLW k
Operands: 0 <= k <= 255
Operation: k -> (W)
Status: None
Encoding: 11 0000 kkkk kkkk
Words: 1
Cycles: 1
Example:
MOVLW 0x5A
After Instruction
W = 0x5A

## Slide 33
PIC MCU Instruction Set Literal Operations
IORLW Inclusive OR Literal with W
Syntax: IORLW k
Operands: 0 <= k <= 255
Operation: (W) .OR. k -> (W)
Status: Z
Encoding: 11 1000 kkkk kkkk
Words: 1
Cycles: 1
Example:
IORLW B’00110101’
Before Instruction
W = B’10001010’
After Instruction
W = B’10111111’
Z = 0

## Slide 34
PIC MCU Instruction Set Literal Operations
ADDLW Add Literal with W
Syntax: ADDLW k
Operands: 0 <= k <= 255
Operation: (W) + k -> (W)
Status: C,DC,Z
Encoding: 11 1110 kkkk kkkk
Words: 1
Cycles: 1
Example:
ADDLW 0x15
Before Instruction
W = 0x10
After Instruction
W = 0x25

## Slide 35
PIC MCU Instruction Set Literal Operations
SUBLW Subtract W from Literal
Syntax: SUBLW k
Operands: 0 <= k <= 255
Operation: k - (W) -> (W)
Status: C,DC,Z
Encoding: 11 1100 kkkk kkkk
Words: 1
Cycles: 1
Example:
SUBLW 0x02
Before Instruction
W = 2
C = ?
Z = ?
After Instruction
W = 0x00
C = 0
Z = 1

## Slide 36
PIC MCU Instruction Set Literal Operations
ANDLW AND Literal with W
Syntax: ANDLW k
Operands: 0 <= k <= 255
Operation: (W) .AND. k -> (W)
Status: Z
Encoding: 11 1001 kkkk kkkk
Words: 1
Cycles: 1
Example:
ANDLW B’01011111’
Before Instruction
W = B’10100011’
After Instruction
W = B’00000011’

## Slide 37
PIC MCU Instruction Set Literal Operations
XORLW Exclusive OR Literal with W
Syntax: XORLW k
Operands: 0 <= k <= 255
Operation: (W) .OR. k -> (W)
Status: Z
Encoding: 11 1010 kkkk kkkk
Words: 1
Cycles: 1
Example:
XORLW B’10101111’
Before Instruction
W = B’10110101’
After Instruction
W = B’00011010’

## Slide 38
PIC MCU Instruction Set Control Operations
k
14-bit Instruction for RETLW
OP CODE
k
k
k
k
k
k
k
k = 8-bit Immediate Value
SLEEP -
CLRWDT -
RETLW k
RETFIE -
RETURN -
CALL k
GOTO k
Control
Operations
14-bit Instruction for CALL and GOTO
OP CODE
k = 11-bit Immediate Value
k
k
k
k
k
k
k
k
k
k
k

## Slide 39
PIC MCU Instruction Set Control Operations
SLEEP Enter SLEEP mode
Syntax: SLEEP
Operands: None
Operation: 00h -> WDT
1 -> TO
0 -> PD
Status: TO, PD
Encoding: 00 0000 0110 0011
Words: 1
Cycles: 1
Example:
SLEEP

## Slide 40
CLRWDT Clear Watchdog
Syntax: CLRWDT
Operands: None
Operation: 00h -> WDT
0 -> WDT prescaler
1 -> TO
1 -> PD
Status: TO, PD
Encoding: 00 0000 0110 0100
Words: 1
Cycles: 1
PIC Instruction Set Control Operations
Example:
CLRWDT

## Slide 41
PIC MCU Instruction Set Control Operations
RETLW Return with Literal in W
Syntax: RETLW k
Operands: 0 <= k <= 255
Operation: k -> (W)
TOS -> PC
Status: None
Encoding: 11 0100 kkkk kkkk
Words: 1
Cycles: 2
Example:
RETLW 0x5A
After Instruction
W = 0x5A

## Slide 42
PIC MCU Instruction Set Control Operations
RETFIE Return from Interrupt
Syntax: RETFIE
Operands: None
Operation: TOS -> PC
1 -> GIE
Status: None
Encoding: 00 0000 0000 1001
Words: 1
Cycles: 2
Example:
RETFIE

## Slide 43
PIC MCU Instruction Set Control Operations
RETURN Return from Subroutine
Syntax: RETURN
Operands: None
Operation: TOS -> PC
Status: None
Encoding: 00 0000 0000 1000
Words: 1
Cycles: 2
Example:
RETURN

## Slide 44
PIC MCU Instruction Set Control Operations
CALL Call Subroutine
Syntax: CALL k
Operands: 0 <= f <= 2047
Operation: (PC) + 1 -> TOS
k -> PC<10:0>
PCLATH<4:3 -> PC<12:11>
Status: None
Encoding: 10 0kkk kkkk kkkk
Words: 1
Cycles: 2
Example:
Here CALL There
Before Instruction
PC = address Here
After Instruction
PC = address There
TOS = address Here+1

## Slide 45
PIC MCU Instruction Set Control Operations
GOTO Unconditional Branch
Syntax: GOTO k
Operands: 0 <= f <= 2047
Operation: k -> PC<10:0>
PCLATH<4:3> -> PC<12:11>
Status: None
Encoding: 10 1kkk kkkk kkkk
Words: 1
Cycles: 2
Example:
GOTO There
After Instruction
PC = address There

## Slide 46
PIC Instruction Set Byte-Oriented Operations
14-bit Instruction for Byte Oriented Operations
OP CODE
d
f
f
f
f
f
f
f
d = Destination Bit
d = 0 for destination W
d = 1 for destination f
f = 7-bit Register Address
Example:
ADDWF REG, W
ADDWF f, d
NOP -
MOVWF f
CLRW -
CLRF f
SUBWF f,d
DECF f,d
IORWF f,d
ANDWF f,d
XORWF f,d
ADDWF f,d
MOVF f,d
COMF f,d
INCF f,d
DECFSZ f,d
RRF f,d
RLF f,d
SWAPF f,d
INCFSZ f,d
Byte-Oriented
Operations

## Slide 47: 12-bit Core Instruction Set: Byte-Oriented Operations
Byte-Oriented Operation
NOP - No Operation
MOVWF f Move W to f
CLRW - Clear W
CLRF f Clear f
SUBWF f,d Subtract W from f
DECF f,d Decrement f
IORWF f,d Inclusive OR W and f
ANDWF f,d AND W and f
XORWF f,d Exclusive OR W and f
ADDWF f,d Add W and f
MOVF f,d Move f
COMF f,d Complement f
INCF f,d Increment f
DECFSZ f,d Decrement f, skip if zero
RRF f,d Rotate right f
RLF f,d Rotate left f
SWAPF f,d Swap halves f
INCFSZ f,d Increment f, skip if zero
11 6 5 4 0
OPCODE d fffff
d = 0 for destination W
d = 1 for destination f
f = file register address
Notes: Explain the break out of the bits and how it relates to the architecture. I.e. the limited number of bits avail for address effects paging and banking. Also go over the use of the destination bit.

## Slide 48
PIC Instruction Set Bit-Oriented Operations
14-bit Instruction for Bit Oriented Operations
OP CODE
b
f
f
f
f
f
f
f
b = 3-Bit Address
(Bit Number)
f = 7-bit Register Address
b
b
Example:
BTFSC STATUS, C
BTFSC f, b
BCF f,b
BSF f,b
BTFSC f,b
BTFSS f,b
Bit-Oriented
Operations

## Slide 49: 12-bit Core Instruction Set: Bit-Oriented Operations
Bit-Oriented Operation
BCF f,b Bit clear f
BSF f,b Bit set f
BTFSC f,b Bit test f, skip if clear
BTFSS f,b Bit test f, skip if set
11 8 7 5 4 0
OPCODE bbb fffff
f = file register address
b = bit address
Notes: Explain how relates to individual bits addressed.

## Slide 50
PIC Instruction Set Literal and Control Operations
k
14-bit Instruction for Literal Operations
OP CODE
k
k
k
k
k
k
k
k = 8-bit Immediate Value
Example:
MOVLW 0x2F
MOVLW k
SLEEP -
CLRWDT -
RETLW k
RETFIE -
RETURN -
CALL k
GOTO k
MOVLW k
IORLW k
ADDLW k
SUBLW k
ANDLW k
XORLW k
Literal and Control
Operations

## Slide 51: 12-bit Core Instruction Set: Literal and Control Operations
Literal and Control Operations
OPTION - Load OPTION register
SLEEP - Go into Standby Mode
CLRWDT - Clear Watchdog Timer
TRIS f Tri-state™ Port f
RETLW k Return, place Literal in W
CALL k Call Subroutine
GOTO k Go to address (k is 9 bits)
MOVLW k Move Literal to W
IORLW k Inclusive OR Literal and W
ANDLW k AND Literal W
XORLW k Exclusive OR Literal W
11 8 7 0
OPCODE kkkk kkkk
k = literal value
Note: In GOTO instruction,
literal is 9 bits long
Notes: Explain how literal byte handled in opcode.

## Slide 52: 12-bit Core Instruction Set: Branch Instructions
CALL opcode uses 8-bits for address -> Address for routine must be in 1st 256 locations for each page. PC<8> = 0.
GOTO opcode uses 9-bits for address -> Address any location in a page
PC<10:9> comes from PA1:PA0 (STATUS<6:5>)
0
PC
10
9
8
7
0
Call or Modify PCL Instruction
STATUS<PA1:PA0>
From Instruction OP Code
Bits
PC
10
9
8
7
0
Goto Instruction
STATUS<PA1:PA0>
From Instruction OP Code
Bits
Notes: Remind of connection to architecture and paging/banking.

## Slide 53: 12-bit Core Instruction Set: Example #1
RRF Temp, W
Before Instruction:
Temp = b’10100101’
W = ?
C = 0
After Instruction:
Temp = b’10100101’
W = b’01010010’
C = 1
Note: Contents of Temp did not change

## Slide 54: 12-bit Core Instruction Set: Example #2
Move a value from CONTROL to PORTB
Movf CONTROL,W
Movwf PORTB
Before Instruction 1:
CONTROL = b’10100101’
W = ?
PORTB = ?
Z = ?
C = ?
After Instruction 1:
CONTROL = b’10100101’
W = b’10100101’
PORTB = ?
Z = 0
C = 0
Before Instruction 2:
CONTROL = b’10100101’
W = b’10100101’
PORTB = ?
Z = 0
C = 0
After Instruction 2:
CONTROL = b’10100101’
W = b’10100101’
PORTB = b’10100101’
Z = 0
C = 0
Notes: Ask students what happens anytime a value goes thru the W register?
Status bits get set.

## Slide 55: 12-bit Core Instruction Set: Example #3
DECFSZ Temp, F
GOTO NOTZERO
GOTO ZERO
Note: Contents of Temp does change
What are the instructions DECFSZ and INCFSZ useful for?
NOTZERO
ZERO

## Slide 56: Assembler Directives
LIST
  Syntax: list [<list_option>,…list_option>]
  Ex: list p=16F84A, f=INHX8M, r=DEC
  Description: Select various assembler options
INCLUDE
  Syntax: include “filename.*” or <filename.*>
  Ex: include <p16f84a.inc>
  Description: Assembles the indicated file as if it were in-line code in the source file. Commonly used to create modular code segments.
Notes: Explain assembler directives and why used.
Explain difference between “ “ and < >
< > means file is in default mplab directory

## Slide 57: Assembler Directives
ORG
  Syntax: ORG <address>
  Ex: ORG 0x00
  Description: Start assembling the lines below this statement at location 0x00.
EQU
  Syntax: <label> equ <expr>
  Ex: SECONDS equ 0x24
  Description: Define a text substitution for a constant or variable. Seconds is a constant of 24h or is a register @ address 0x24.
    movlw SECONDS ;const = 24h
    movf SECONDS,W ;value in seconds reg.
Notes: Use data sheets as needed to explain fractured memory (step over interrupt vector, etc. ) and no overrun. Also use data sheets to explain manual address assign vs auto assign from next slide.

## Slide 58: Assembler Directives
CBLOCK
  Syntax: cblock [<expr>]
  Example:
    cblock 0x20 ;Start point of cblock
        hours
        minutes
        seconds
        halfseconds:2
    endc ;Indicates end of cblock
  Description: Declare Symbol Constant

## Slide 59: Assembler Directives (cont)
END
  Syntax: end
  Example: Indicates end of source code.
You must have this statement after the last instruction you want assembled.
Notes: Explain how this directive actually tells the compiler to skip all codes below it.

## Slide 60: Relocatable Code What is it?
Code written to work at any address
In source, code and data are organized into blocks called ‘sections’
The linker assigns sections into memory regions

## Slide 61: Relocatable Code Why use it?
Organization - You can organize your project into multiple files
Reusability - Source files can have a more focused purpose, encouraging code reuse
Faster Development - Recompilation of entire project is not required each time a change is made
Convenience - User does not need to organize and manage individual memory locations

## Slide 62: Relocatable Code In MPASM
CODE - Declares the beginning of a program code section
UDATA - Declares the beginning of an uninitialized data section
BANKSEL - Selects the correct bank for a RAM access
PAGESEL - Selects the correct bank for a ROM access
EXTERN - Indicates a variable that is declared in another module
GLOBAL - Indicates that a variable is referenced in another module