## Slide 1: On to the Labs

## Slide 2: Lab 1 PIC12C672 14-bit core
Notes: In each of the steps following for lab 1, have the students watch first then do the actions of their machines.

## Slide 3: Lab1
Objective:
Program an OTP and plug it into your PIC & Stick take home demo board
  1st time experience with tools
  Will use PIC & Stick board with non-coded PIC’s
Notes: Teach students how to setup a project file, build project, program part. General tools usage. Use picNstick with the non-coded pics. Go thru a review of what each of the buttons are and do. Especially when using the simulator.

## Slide 4: Lab 1 MPLAB Layout
Development Mode
Target Processor
Run
Halt
Step
Reset
Make

## Slide 5: Lab 1 Selecting Hardware Options
Use Debugger > Select Tool > MPLAB SIM… to select execution environment
Use Configure > Select Device to select processor
Use Debugger > Settings > Clock TAB to select oscillator frequency
  MPLAB-ICE uses a programmable clock
  MPLAB-SIM only uses frequency for time calculations

## Slide 6: Lab 1 MPLAB Projects
MPLAB projects manage:
  Installed build tools
  Development mode
  Hardware settings
  Source files
  Dependencies (*.inc, *.h)
  Compile, link, and assembly options

## Slide 7: Lab 1 Creating a New Project
Choose Project > New Project… from the menu, and select a filename for your project

## Slide 8: Lab 1 Setting Build Options

## Slide 9: Lab 1 Configuring Build Tools
Microchip’s tools are configured for use during installation
For other tools, use Project > Select Language Tool Suite...
Use the Active Toolsuite: pulldown bar for other Language toolsuites

## Slide 10: Lab 1 Using the Project Window
Quick access to project summary
  Source files
  Dependencies

## Slide 11: Setting Up MPLAB Projects Program Your Part
Verify that your program is listed in the “Program Memory Window”
If it is not, build your project again to update the “Program Memory Window”
Verify device settings in the PICSTART Plus Device Programmer window
Insert part to be programmed with correct pin 1 orientation
Click on Program to program part

## Slide 12: Lab notes
Must make a project first, prior to programming part
Make sure that the .asm file is listed in the project as a file to be built
Must build the .asm file to create a .hex file prior to programming part
Make sure that correct part is selected on programmer
Must set configuration bits for the operating mode of the part

## Slide 13: What feature set (reminder)
  Open/close
  Switch controlled
  Held open to allow passage thru door
  Automatic close (store type)
  Safety cutoffs (if time permits)
  Independent motor control (if time permits)
  Double tap (if time permits)
  Lighting control (optional)
  Sound control* (optional)
Notes: Note to students that from lab 2 on, all of the work they do is heading towards the final project so review the final project specs. Mention/elicit from students what aspects, switching, timing, etc are uesd to achieve each of the project specs.

## Slide 14: Lab 2 Using An I/O Port (Switching) PIC12F508 12-bit Core

## Slide 15: Lab notes: Peripheral Used: Digital I/O Ports
6 - 20 I/O pins
Each I/O pin software configurable as input or output
Direct bit manipulation (single-word/single-cycle):
Bit set
Bit clear
High drive capability
  25mA sink max (all parts)
  60mA sink max (PIC17CXXX)
  25mA source max
Can directly drive LEDs:
Notes: <number>
<footer>
<header>
<date/time>
On reset I/O are defaulted to High Impedance inputs
NOTE: Each pin has a high drive capability, but Ports also have current maximums (due to Vdd/Vss electromigration issues - device reliability issue).

## Slide 16: Peripherals: Digital I/O Port (Cont.)
Data Bus
Wrt. Port
D
Q
Q
SET
CLR
D
Q
Q
SET
CLR
W Reg
Tris f
Rd. Port
I/O Pin
Data Latch
Tris Latch
Vss
Vdd
Reset
Notes: <number>
<footer>
<header>
<date/time>
I/O pin structure
When pin is in Reset start, the pin is a high impedance input (both transistors are turned off)

## Slide 17: Lab Notes: Read-Modify-Write
PC
PC + 1
PC + 2
PC + 3
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Instruction
fetched
RB7:RB0
MOVWF PORTB
write to
PORTB
NOP
Port pin
sampled here
NOP
MOVF PORTB,W
Instruction
executed
MOVWF PORTB
write to
PORTB
NOP
MOVF PORTB,W
PC
TPD
Note:
This example shows a write to PORTB
followed by a read from PORTB.
Note that:
data setup time = (0. 25TCY-TPD )
where
TCY= instruction cycle
TPD = propagation delay
Therefore, at higher clock frequencies,
a write followed by a read may be problematic.
Consider loads on pins for back to back read-modify-writes
Qcy = Fosc
Instruction cycle = Fosc/4
Notes: Explain read modify write. Use example of stray capacitance on a pin being written to then read with no nop in between and how the rc curve effects the read back value.

## Slide 18: Workshop Board Schematic (excerpt)

## Slide 19: Lab2 Using An I/O Port
Objective:
Drive port pin GP4 to a logic 1
Verify code with the MPLAB Simulator
Program a part and test it in your workshop board
Notes: All labs from lab2 on out are to develop modules. The latter labs will have the students combining the modules to handle base functions and adding features modules as each new set of functions are added.

## Slide 20: Make a project file review

## Slide 21: Setting Up MPLAB Projects Make A .asm File
File -> New
  This opens a text window where you can begin entering your code
Type in program header
File -> Save As
  Save the file as lab2.asm
File -> Close

## Slide 22: Setting Up MPLAB Projects Make A Project File
Project -> New
  Type Lab2 in Project Name Box
  Click Browse: Find Folder: C:\PIC101 Click the Select button
    Click on OK
  Project Files
    Right Click on Source files
      Select Add Files
      Find Lab2.asm Click Open
Notes: This review is in as needed. Is recommended to have them watch instructor as he runs thru making a project but with lab2 file names. Then have the students do it. Is a good reminder.

## Slide 23: Setting Up MPLAB Projects Make A Project File (cont.)
  Project Files Continued
    Right Click on Header files
      Select Add Files
      Find c:\Program Files\MPLAB IDE\MCHIP_tools\P12C508A.inc
      Click Open
Notes: This review is in as needed. Is recommended to have them watch instructor as he runs thru making a project but with lab2 file names. Then have the students do it. Is a good reminder.

## Slide 24: Setting Up MPLAB Projects Make A Project File (cont.)
  Project Files cont.
    Debugger > Select Tool > MPLAB SIM
    Configure > Select Device
      Use Device: pull down Bar
        Select the appropriate part [12F508A]
        Click on OK (Close Select Device Dialogue box)

## Slide 25: Setting Up MPLAB Projects Verify Correct .asm File
Verify that the “Node: lab2.asm” file is the correct file you are working on.
Double click on lab2.asm in the Lab2.mcw Project window
  Lab2.asm will be used for this project

## Slide 26: Code Ex2 - Light an LED
  ;**********************************************************************
  ;This program drives a 1 onto port pin GP4
  ;**********************************************************************
  List P=12F508, R=hex
  include <P12F508.inc> ;load the include file
  __CONFIG _IntRC_OSC & _WDT_OFF & _CP_OFF & _MCLRE_ON
org 0x00 ;indicate the start location
Start clrf GPIO ;load output latch w/zeros
movlw 0x00 ;Configure port to outputs
tris GPIO ;
bsf GPIO,4 ;set pin 4 on GPIO (GP4) to logic 1
Loop nop
goto Loop ;$ = current address... infinite loop
end
Notes: This is where I have the students fire up MPLAB and I walk them through setting up a project and creating a file with the above code. Finish all of the slides including the review of the simulator’s controls before having them type in the above code. We will go back to this slide after the sim review.
Go over the above code to illustrate the minimum requirements of an assembly file.
Use MPLAB-SIM’s watch windows to illustrate the how the above code executes the part.

## Slide 27: Create a Watch Window
View -> Special Function Registers
View -> Watch -> New Watch Window
  Use pull down menu to select registers/variables to watch
  Click Add FSR button after each one or Click Add Symbol button
Notes: Show how to view bin vs hex

## Slide 28: Use simulator to step thru the code
Debugger -> Run
  F6 Reset
  F7 Step
  F8 Step Over
  F9 Run
  F5 Halt
  Ctrl + F9 Animate
Notes: Review simulator buttons and other general controls.

## Slide 29: Lab notes
Must declare org statements so assembler knows code/memory organization
Don’t forget to declare variables if needed
Must configure port pins prior to writing to them

## Slide 30: Lab3 Timing PIC12F508 12-bit Core

## Slide 31: Lab notes: Peripheral Used: TMR0
Readable and writable
Generates interrupt on overflow from FFh to 00h
Prescaler is programmable
In timer mode: fastest increment rate is OSC/4 (5 MHz @ 20 MHz oscillator frequency)
In counter mode: configurable to increment on either edge
External counter mode has Max. input = 50 MHz (using prescaler)
Writing to TMR0 causes an error of 2 Tcy
Ext clock
input
Internal clock
8-bit prescaler
8-bit timer/counter
Interrupt on overflow (not on PIC12C508A)
Notes: <number>
<footer>
<header>
<date/time>
A write to TMR0, automatically clears the prescaler. After a write to the TMR0, there is a 2 cycle delay before a actual increment occurs, this has to be taken into account for accurate time measurements.
The prescaler is asynchronous. The input clock to the TMR0 register is synchronized after the prescaler
So if an external clock source is selected, higher clock frequencies then the device frequency can be used (frequency depends on prescaler value).
The value of the prescaler is not readable

## Slide 32: Lab Notes:
Timing Loop
Counting Loop
Nested Loop
Branch Control
BTFSS
BTFSC
DECFSZ
INCFSZ
Notes: Explain how timing/counting/nested loops work. Why they are good for quick and dirty timing but how they tie up processor and burn up cycles which could have been used for something else.

## Slide 33
OPTION REG
PIC12F508
W-1
W-1
W-1
W-1
W-1
W-1
W-1
W-1
GPWU
GPPU
T0CS
T0SE
PSA
PS2
PS1
PS0
W= Writable bit
U= Unimplemented bit
- n= Value at POR reset
Reference Table4-1 for other
resets.
bit7
6
5
4
3
2
1
bit0
bit
5:
T0CS
: Timer0 clock source select bit
1 = Transition on T0CKI pin
0 = Transition on internal instruction cycle clock, Fosc/4
bit
4:
T0SE
: Timer0 source edge select bit
1 = Increment on high to low transition on the T0CKI pin
0 = Increment on low to high transition on the T0CKI pin
bit
3:
PSA
: Prescaler assignment bit
1 = Prescaler assigned to the WDT
0 = Prescaler assigned to Timer0
bit
2-0:
PS2:PS0
: Prescaler rate select bits
000
001
010
011
100
101
110
111
1
:
2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
1 : 256
1 : 1
1 : 2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
Bit Value
T
imer0
Rate
WDT Rate
Notes: Review control bits in option register. Explain how on 12bit cores the option is a command but on 14bit core it is a register. (option_reg) use data sheets to show difference. Will remind them of diference in latter lab.
Cover other items like woc, pullups, etc.

## Slide 34: Lab3 Timing
Objective
Write an approx. 2 ms delay loop program using TMR0
  Typically used to
    provide timing for delaying/controlling events
    provide timing for tracking events
Do not use the prescaler
Pre-load TMR0 to count 200 micro seconds
Light 2 LEDs to indicate status
  GP4 LED2 should light to indicate that your program is running
  GP5 LED1 should light when the approx. 2 ms delay has occurred
Verify using MPLAB simulator with stopwatch
Notes: Use tmr0 module and also highlight how this can be done w/ no interrupts (12bit core). Go thru timing calculations with class.

## Slide 35: Lab notes: Calculate # of TMR0 Roll Overs
Part uses a 4Mhz clock
TMR0 clocks @ a rate of Fosc/4
  if prescaler not used
TMR0 rolls over from FFh to 00h
How many counts does a s/w counter need to get approx. 2 ms?
How many counts does a s/w counter need to get approx. 2 ms if tmr0 only counts 200 micro seconds?

## Slide 36: Code Ex3 - 2 ms delay
;***************************************************************
;approx. 2 ms delay program with 2 status leds to show start and end of delay
;***************************************************************
  List P=12F508, R=hex
  include “P12F508.inc” ;load the include file
  __CONFIG _IntRC_OSC & _WDT_OFF & _CP_OFF & _MCLRE_ON
  cblock 0x07
  COUNTER
  endc
  Org 0x00
  movwf OSCCAL ;setup INTRC calibration
  .
  .
  Place your code here
  .
  .
  end
Notes: Have them use the lab3 template already created.

## Slide 37: Code Ex3 - 2 ms delay (cont.)
Set Prescaler
Light 1st LED
Reset TMR0
2
ms?
Light 2nd LED
Notes: Review how flow chart breaks down the problem into manageable pieces.

## Slide 38: Lab notes
  The PIC12F508A has an 8 bit timer (TMR0) with a selectable prescaler (up to 8 bits)
  You may need to pre-load TMR0 to get the desired time
Notes: The purpose of this exercise is to illustrate how additional hardware peripherals can off-load the processor so that it is available to handle multiple tasks at the same time.
Start by explaining the concept of interrupts and that we use them to allow hardware peripherals to perform fixed tasks without loading the processor’s core.
Explain the TMR0 peripheral and how we could use it to count instruction cycles while we do something else in the main routine. It may take a while to explain the prescaler’s function and how to set it up.
Explain the GIE and T0IE. Explain how the T0IF bit works.
Write the code.

## Slide 39: Lab notes: Sample window
What happens if the FFh -> 00h roll over occurs after you have sampled?
Use a Sample Window
Notes: Explain how since no interrupts how to handle tmro roll over events before letting students start writing code. Will go back to template slide if needed.
Before release students to write code, have them setup processor options. INTRC, stack overflow, etc.

## Slide 40: Lab3 Timing
Review sample code lab3.asm provided by the instructor.
Notes: Give them 20-30 min to attack the problem then review the insturctors lab3.asm explaining why things were done the way they were. Be sure and review sample window. Show how to use stop watch to verify time.

## Slide 41: Lab4 Timing PIC16F84A 14-bit Core
Notes: Lab 4 introduces interrupts. Has students do same thing as lab3 but with interrupts.

## Slide 42: Feature Used: Interrupts
RBIF
RBIE
T0IF
T0IE
INTF
INTE
GIE
EEIE
Wake
-
up
(If in SLEEP mode)
Interrupt to CPU
EEIF

## Slide 43
INTCON REG
PIC16F84A
R/W-0
R/W-0
R/W-0
R/W-0
R/W-0
R/W-0
R/W-0
R/W-x
GIE
EEIE
T0IE
INTE
RBIE
T0IF
INTF
RBIF
R= Readable bit W= Writable bit
U= Unimplemented bit, read as ‘0’
- n= Value at POR reset
bit7
bit0
bit 7:
GIE:
Global Interrupt Enable bit
1 = Enables all un-masked interrupts
0 = Disables all interrupts
bit 5:
T0IE
: TMR0 Overflow Interrupt Enable bit
1 = Enables the TMR0 interrupt
0 = Disables the TMR0 interrupt
bit 2:
T0IF
: TMR0 Overflow Interrupt Flag bit
1 = TMR0 has overflowed (must be cleared in software)
0 = TMR0 did not overflow
Notes: Review intcon bits.

## Slide 44
OPTION REG
PIC16F84A
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
R/W-1
RBPU
INTEDG
T0CS
T0SE
PSA
PS2
PS1
PS0
R= Readable bit W= Writable bit
U= Unimplemented bit, read as ‘0’
- n= Value at POR reset
bit7
bit0
bit
5:
T0CS
: TMR0 Clock Source Select bit
1 = Transition on RA4/T0CKI pin
0 = Internal instruction cycle clock (CLKOUT)
bit
4:
T0SE
: TMR0 Source Edge Select bit
1 = Increment on high-to-low transition on RA4/T0CKI pin
0 = Increment on low-to-high transition on RA4/T0CKI pin
bit
3:
PSA
: Prescaler Assignment bit
1 = Prescaler assigned to the WDT
0 = Prescaler assigned to TMR0
bit
2-0:
PS2:PS0
: Prescaler Rate Select bits
000
001
010
011
100
101
110
111
1 : 2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
1 : 256
1 : 1
1 : 2
1 : 4
1 : 8
1 : 16
1 : 32
1 : 64
1 : 128
Bit Value
TMR0 Rate
WDT Rate
Notes: Review option bits.

## Slide 45: Workshop Board Schematic (excerpt)

## Slide 46: Why Interrupts
Better use of CPU resource
Faster response time
Multi-tasking
Fixed or known interval handler
Exception handler

## Slide 47: Lab notes: Interrupt Service Routines; Context Changes
Push macro
movwf W_TEMP ;push W and STATUS
swapf STATUS,W ;
movwf STATUS_TEMP ;
endm
Pop macro
swapf STATUS_TEMP,W ;pop W and STATUS
movwf STATUS ;
swapf W_TEMP,F ;
swapf W_TEMP,W ;
endm
Notes: Explain context changes. Have students answer why important.

## Slide 48: Lab4 Timing
Objective
Write an approx. 2 second delay loop program using TMR0 and interrupts
  typically used to
    provide timing for delaying/controlling events
    provide timing for tracking events
Use prescaler
Light 2 LEDs to indicate status
  RB2 LED1 should light to indicate that your program is running
  RB3 LED2 should light when the approx. 2 sec delay has occurred
Verify using MPLAB simulator and on your workshop board when finished
Notes: Use tmr0 module and also highlight usage of interrupts. Go thru timing calculations with class.

## Slide 49: Lab notes: Calculate # of TMR0 Roll Overs
Part uses a 4Mhz clock
TMR0 clocks @ a rate of Fosc/4
  if prescaler not used
TMR0 rolls over from FFh to 00h
Prescaler set to max
How many counts does a s/w counter need to get approx. 2 sec.?

## Slide 50: Code Ex4 - 2 sec delay
;***************************************************************
;approx 2 sec delay program using interrupts with 2 status leds to show start and end of delay
;***************************************************************
  List P=16F84A, R=hex
  include “p16f84a.inc” ;load the include file
  __CONFIG _XT_OSC & _WDT_OFF & _CP_OFF & _PWRTE_ON
  cblock 0x0C
  COUNTER
  W_TEMP
  STATUS_TEMP
  endc
  Org 0x00
  goto Start
  Org 0x04
  goto Int_serv_routine
Notes: This template provided. Just review structures. Students do need to type this in.

## Slide 51: Code Ex4 - 2 sec delay
  Org 0x05
  Start
  .
  .
  Place your code here
  .
  .
  Int_serv_routine
  .
  .
  Place your code here
  .
  .
  end

## Slide 52: Code Ex4 - 2 sec delay (cont.)
Set Prescaler
Light 1st led
Reset TMR0
Wait for
Interrupt
Light 2nd led
Setup Interrupts
What
caused Int
ISR
2
sec?
Notes: Review flow chart again. Re-explain how this helps.

## Slide 53: Lab notes
  The 16F84A has an 8 bit timer (TMR0) with a selectable prescaler (up to 8 bits)
  You may need to pre-load TMR0 to get the desired time
  The main program should be an endless loop (goto $)
  The interrupt vector is address 0x04
  Assert RB3 in the Interrupt Service Routine as status indicator
  Keep ISR as simple as possible. Fill with calls as needed.
Notes: The purpose of this exercise is to illustrate how additional hardware peripherals can off-load the processor so that it is available to handle multiple tasks at the same time. Explain goto $ and how it helps.
Start by explaining the concept of interrupts and that we use them to allow hardware peripherals to perform fixed tasks without loading the processor’s core.
Explain the TMR0 peripheral and how we could use it to count instruction cycles while we do something else in the main routine. It may take a while to explain the prescaler’s function and how to set it up.
Explain the GIE and T0IE. Explain how the T0IF bit works.
Write the code.

## Slide 54: Lab4 Timing
Review sample code lab4.asm provided by the instructor.
Notes: Give students about 20-30 minutes to hack at this one. Then review the instructors lab4 code.

## Slide 55: Lab5 Motor Control PIC16F84A 14-bit Core

## Slide 56: Motor Connection Schematic

## Slide 57: Lab5 apply to simple motor control
Objective
Apply labs 2 and 4 to control door motors
Motor control to drive doors both open and close
Toggle opening and closing of door in a repeating cycle
Validate using MPLAB simulator, your workshop board, and the scale model prototype when finished
Notes: Students need to beware that there are 2 motors that they need to drive simultaneously. Porta is wired to the 2 motors with pins <1:0> tied to motor left and pins <3:2> tied to motor right.
Students should use workshop board for this lab. Explain features of the workshop board here.
Students should use scale prototype board from labs 6 on as tests of their burned code.
*Note to class
Can be more efficient and design to control motors w/ just 1 pin by using H-bridge but for purposes of class, use 2 pins.

## Slide 58: Lab notes
Motor biasing is set for standard logic
2 control bits are required for each motor
You will need to stop the motion of the motor before reversing it’s direction to avoid stripping motor’s gears
Use the timing and I/O port control modules you developed earlier to help you
PORTA is tied to the 2 door motors
Notes: Must stop motor’s motion to avoid stripping the motors gears.
Note to students that when using the workshop board, only port A is wired to the leds via the c57 part.

## Slide 59: Lab 6 Sensing an Input PIC16F84A 14-bit Core

## Slide 60: Lab6 add sensing/inputs (2 part lab)
Mechanical catch/releases vs electrical switches
Floor pad/wall switch
Input techniques
  polling
  external interrupt on INT pin
  interrupt/wake up on change
Notes: Spend some time going over the different input techniques and advantages and limitations of each. Use following slide as needed.

## Slide 61: Input techniques
Polling
  sample window roll over
  power consumed
  ringing input
  debouncing of input signal
External interrupt on INT pin
  multiple interrupts
  sequential servicing
  simultaneous interrupts
Interrupt/wake up on change
  can put part to sleep prior to receiving interrupt input
  battery type apps

## Slide 62: Lab 6 (a) Polling Input Pin

## Slide 63: Why Debounce?
Ringing inputs
Noisy inputs
Glitch on input

## Slide 64: Debounce push button/key Ringing or noisy inputs
AN 566 contains debounce
Check_key
;poll for key press
btfsc PORTB,1 ;
goto Check_key ;
; call Debounce_delay ;debounce signal
btfsc PORTB,1 ;check for bouncing input
goto Check_key ;
return
;routine to give delay for key bounce routine
Debounce_delay
.
.
delay routine here
.
return
Notes: Use this code to explain how to handle signal bounce.

## Slide 65: Polling Input Schematic

## Slide 66: Lab 6 (a) of 2-step lab
Objective
Read input by polling, (foot pad) to activate door “opening/closing sequence” module you developed earlier
Momentary switch on port pin RB1
RB1 is an active low input
Validate using MPLAB simulator, your workshop board, and scale model prototype when finished

## Slide 67: Code Ex6a - Polling Input
Set Prescaler
Reset TMR0
Wait for
Interrupt
Setup Interrupts
RB1
Lo?
Door Control
State Machine
What
caused Int
ISR
2
sec?
Notes: Review flow chart.

## Slide 68: Lab notes
Call a input checking routine from your main loop
Might need a state machine to track the different phases (open, close, etc.) and coordinate with your timing routines
Must loop back to look for next input

## Slide 69: Lab 6 (b) Interrupt on INT Pin

## Slide 70: Feature Used: Interrupt on INT Pin PIC16F84A
RBPU
(1)
I/O
pin(2)
Data Latch
P
VDD
Q
D
CK
Q
D
Q
D
EN
Data bus
WR Port
WR TRIS
RD TRIS
RD Port
Weak
pull-up
RD Port
RB0/INT
TTL
Input
Buffer
Schmitt Trigger
Buffer
TRIS Latch
Note 1: TRISB = '1’ enables weak pull-up
(if RBPU = '0' in the OPTION_REG register).
2: I/O pins have diode protection to VDD and VSS.
CK

## Slide 71: INT Pin Schematic

## Slide 72: Lab6 (b) of 2 step lab
Objective
Read input by interrupt on INT pin (optical sensor) to activate door opening/closing module you developed earlier
Light sensor on port pin RB0
RB0 is active low sensor input
Validate using MPLAB simulator, your workshop board, and scale model prototype when finished
Notes: Want to teach them int on int pin.

## Slide 73: Code Ex6b - INT Pin Input
Set Prescaler
Reset TMR0
Sleep or
Wait for
Interrupt
Setup Interrupts
Int on INT pin
Door Control
State Machine
What
caused Int
ISR
2
sec?
TMR0
Notes: Review flow chart.

## Slide 74: Lab notes
Use different setup routines for the different interrupt modes
Might need a state machine to track the different phases (open, close, etc.) and coordinate with your timing routines
Don’t forget to put part to sleep or in a dead loop while waiting for interrupt on INT pin input (don’t overrun into unwanted areas)
Must loop back to look for next input
Notes: They need to control when T0IE and RBIE modes are active.

## Slide 75: Lab7 State Logic/Higher Order Functions PIC16F84A 14-bit Core

## Slide 76
RBPU
(1)
Data Latch
P
VDD
Q
D
CK
Q
D
CK
Q
D
EN
Q
D
EN
Data bus
WR Port
WR TRIS
Set RBIF
TRIS Latch
RD TRIS
RD Port
From other
RB7:RB4 pins
weak
pull-up
RD Port
Latch
TTL
Input
Buffer
I/O
Feature Used: Interrupt On Change PIC16F84A
Note 1: TRISB = '1’ enables weak pull-up
(if RBPU = '0' in the OPTION_REG register).
2: I/O pins have diode protection to VDD and VSS.

## Slide 77: Peripheral Used PortB Interrupt on Change example
Internal pull-ups (software option) keep RB4-RB7 pins high
RB0-RB3 pins drive '0's
Any key pressed pulls down an RB pin and generates an interrupt
This interrupt wakes up processor from SLEEP
Saves timer resources
Keypad interface:
PIC16CXXX
RB0
RB1
RB3
RB4
RB5
RB6
RB7
RB2
Hex keypad
R †
† Resistance for ESD protection
100 
AN557
Notes: <number>
<footer>
<header>
<date/time>
This example shows how the internal pull-up resistors on RB7-RB4 can be used in conjuction with the change of PortB interrupt to wake the device from sleep when a key is hit.

## Slide 78: Interrupt On Change Schematic

## Slide 79: Lab7 State logic/higher order functions
Objective
Delay to hold door open approx 2 seconds before auto closing
Use “interrupt on INT pin” input method from Lab6(b) to start door sequence
Option 1
  Motor cutoffs
    Position feed back
    Use interrupt on change
Notes: Emergency cut offs are momentary switches tied to the INT on change pins of the pic (RB7:RB4). Explain why might want independent morot controls. Show how this works on workshop board and on scale prototype.
Instructors lab 8 only implements 2 sec delay to hold doors open to let people to walk thru. Instructors lab9b shows full functionality with position feedback, independent motor control, and 2 sec safety hold of door if someone in the way.

## Slide 80: Lab7 State logic/higher order functions
Objective (cont.)
Option 2
  Do not close doors if INT pin sensor still active
  Safety feature
  People still in the doorway
Option 3
  Independent motor cutoff
  Different motor speeds
Validate using MPLAB simulator, your workshop board, and scale model prototype when finished

## Slide 81: Lab notes
Might need a state machine to track the different phases (open, hold open, close, etc.) and coordinate with your timing routines
Use different setup routines for the different interrupt modes
If adding motor cutoffs (option1), don’t use timing delay module while motors running (open or close). But use timing delay to hold door open for 2 sec.
Safety check (option2) only applies when closing doors

## Slide 82: Lab8 Proof Final Functionality PIC16F84A 14-bit Core

## Slide 83: Lab8 combine labs 6 & 7
Objective
Demonstrate final functionality of automatic door controller on workshop prototype board
  Combine all of the developed modules
  Demonstrate optional features if developed (I.e. emergency cutoffs, access light, double tap logic)

## Slide 84: If time permits, discuss a hypothetical design (I.e. home heating/cooling controller) from start to finish

## Slide 85: MCU Robust Design Techniques

## Slide 86: Robust Design Techniques Watchdog Hardware
Helps recover from software malfunction
Uses its own free-running on-chip RC oscillator
WDT cannot be disabled by software
WDT overflow resets the chip
CLRWDT instruction clears WDT
Programmable time-out period: 18 ms to 2.5 seconds
Operates in SLEEP
On time-out wakes up CPU
8-bit ripple counter
"CLRWDT"
Reset
Overflow
resets
chip
Postscaler
RC
oscillator
Notes: <number>
<footer>
<header>
<date/time>
The WDT and TMR0 share the same 8 bit pre-scaler.
A WDT time-out from SLEEP will not cause a reset, but continuation of the program at the next instruction after sleep.
Note: most of the issues with re-assignment of the pre-scaler have been covered in the TMR0 section.

## Slide 87: Robust Design Techniques Watchdog Software Strategies
Watchdog effectivness is only as good as the software controlling it
Use one CLRWDT instruction for the entire program
Place CLRWDT in the main loop
Do not place CLRWDT in ISR or any sub-routines
Select the minimum WDT timeout period that main loop timing can tolerate
Initialize unused memory as GOTO wdtreset (self-loop) to force timeout

## Slide 88: Robust Design Techniques Robust Software - Filling Unused Memory
When using watchdogs, fill unused memory locations with a GOTO wdtreset
This self loop is normally never executed
If the PC is corrupted, it is likely it will execute this instruction
  Force a WDT reset to re-initialize the core
FILL can be used to insert these instructions (Substitute <last location+1> for 400h):
FILL (GOTO wdtreset), (400h-$)
ORG 3FFh

## Slide 89: Robust Design Techniques Robust Software - Clean WDT reset
To force WDT reset on power-up:
  Check for RAM pattern at power-up
  If pattern is not there:
    Initialize RAM pattern
    Force WDT reset
Force WDT reset if code jumps to unused program memory
Notes: <number>
<footer>
<header>
<date/time>
Check for (RAM register) = ADDRESS at power up
If any RAM register NOT EQUAL to address then:
  Initialize RAM register = ADDRESS
  Force WDT reset.
Upon power up, this algorithm will init RAM and then force a WDT reset.
The second time through, it will find all of RAM initialized and fall through.

## Slide 90: Robust Design Techniques Robust Software - Subroutine Counting
Maintain subroutine call and execution counters
Increment call counter for every subroutine call
Increment execution counter at the top of every sub-routine
At the top of main loop, check if call and execution counters are equal
If not equal, force a WDT reset
Code Example: ADVRELSW.ASM

## Slide 91: The End Thanks for attending!
Notes: Remind students to take only the PicDem 1, and uniforce demo board. They are to leave the mplab ice, processor module, and picstart + in the class.

## Slide 92: Appendix

## Slide 93: Glossary
TMR0 - 8-bit timer peripheral w/8 bit prescaler
Prescaler - peripheral which delays the TMR0 count by a prescale ratio i.e. 1:1, 1:2, 1:4
Page - memory organization for program memory
Bank - memory organization for data memory
Pipeline - hardware architecture for prefetching an opcode while executing the previous opcode
Orthogonal instruction set - instructions work on ports and registers the same way
OPTION_REG - register of control bits for configuring tmr0, INT, and pull ups
INTCON - register of control bits for configuring peripheral interrupts
STATUS - register of bits indicating the results of an operation
RP1&RP0 - direct addressing bank selection control bits
IRP - indirect addressing bank selection control bit
PORTB - I/O port B
GPIO - I/O port on the 8 pin parts

## Slide 94
The Microchip name, logo, The Embedded Control Solutions Company, PIC, PIC, PICSTART, PICMASTER, PRO MATE, SEEVAL, KEELOQ and the KEELOQ logo are registered trademarks and MPLAB, fuzzyLAB, In-Circuit Serial Programming, ICSP, are trademarks of Microchip Technology Incorporated in the USA and other countries.
Windows is a registered trademark of Microsoft Corporation.
SPI is a trademark of Motorola.
I2C is a registered trademark of Philips Corporation.
Microwire is a registered trademark of National Semiconductor Corporation.
fuzzyTECH is a registered trademark of Inform Software Corporation.
All other trademarks herein are the property of their respective companies.
© 1999 Microchip Technology Incorporated. All rights reserved.
“Information contained in this publication regarding device applications and the like is intended through suggestion only and may be superseded by updates. No representation or warranty is given and no liability is assumed by Microchip Technology Inc. with respect to the accuracy of such information, or infringement of patents arising from any such use of otherwise. Use of Microchip’s products as critical components in life support systems is not authorized except with express written approval by Microchip. No licenses are conveyed, implicitly or otherwise, under any intellectual property rights.”