## Slide 1: PIC 101
Architecture

## Slide 2: PIC Architecture RISC-like Features
Harvard architecture
Register file concept
All instructions single-word
LWI (Long Word Instruction)
Instruction pipelining
Single-cycle instructions
Reduced instruction set
Orthogonal instruction set
The high performance of the PIC MCU family can be attributed to the following architectural features:
Notes: Reduced Vs Complex instruction set intel 8051 (licensed)
Register as if they are files each have an address
more than 8 bits
Explain orthogonal as there is not a follow on slide covering it. The way you access registers simultaneously

## Slide 3: PIC Architecture Harvard Architecture
Fetches instructions and data from one memory.
  Limits Operating Bandwidth
Two separate memory spaces for instructions and data.
  Increases throughput
  Different program and data bus widths are possible
Program
and Data
Memory
Von Neumann
8-Bits
CPU
Program
Memory
Data
Memory
8-Bits
12/14/16-Bits
Harvard
CPU
Notes: Highlight advantages of the 2 bus methodology.

## Slide 4: PIC MCU Architecture Pipelining
Flush Fetch 4
Fetch SUB_1
In most microcontrollers, instructions are fetched and executed sequentially.
Allows overlap of fetch and execution.
Makes single cycle execution.
Program branches (e.g. GOTO, CALL or Write to PC) takes two cycles.
Tcy0 Tcy1 Tcy2 Tcy3 Tcy4
Execute 1
Fetch 3
1. MOVLW 55h
Fetch 1
Execute 3
Fetch 2
Execute 2
Fetch 4
2. MOVWF PORTB
3. CALL SUB_1
4. BSF PORTA, BIT3
Notes: Cover basic pipeline. Also cover branch conditions and the number of instruction cycles needed for branch taken and branch not taken.

## Slide 5: PIC MCU Architecture Block Diagram
Program
Bus
EPROM
Program
Memory
Clock/Counter
T0CKI
I/O Ports
Ports
Peripheral(s)
Instruction
Decode &
Control
Timing
Generation
MCLR
OSC1
OSC2
Watchdog
Timer
Power-on
Reset
OSC Start
-upTimer
Brown-out
Reset
Program Counter
STACK1
STACKn
STATUS Reg
Mux
W Reg
ALU
MOVF PORTB,W
00100000000110
001000 0 0000110
001000 0
0000110
01010101
01010101
Direct Addr
Addr Mux
RAM
File Registers
Data Bus
Instruction Reg
Indirect Data
Address
FSR
MOVLW 0xAA
11000010101010
MOVF INDF,W
00100000000000
10101010
110000 10101010
001000 0 0000000
000000
110000
001000 0

## Slide 6: PIC Architecture Register File Concept
General Purpose
Registers (RAM)
Other SFRs
PORTA
FSR
STATUS
PCL
TMR0
INDF
W Register
ALU
Data
Memory
Direct data addr <7>
Op code <7>
14-bit Instruction Format Example:
RAM is a bank of general purpose registers.
Peripherals (I/O) are registers.
All instructions operate on any register.
Long word instruction allows direct addressing of registers.
Notes: Highlight register files. Pull examples from data sheets as needed.

## Slide 7: Quiz 1
1) All of Microchip’s PIC instructions are _____.
2) The PIC pipeline must be flushed whenever ____ is modified.
Single Cycle
Single Byte
Single Word
W register
PortB
PC
Notes: Let students work on quiz for 5 min. then review as a group calling on individuals for answers. (interact)
1)word
2)pc

## Slide 8: PIC Architecture
Memory

## Slide 9: PIC Architecture Memory
2 types of memory
  Program
  Data
Organization
  Pages (program)
  Banks (data)
Notes: Explain that mapping methodology used due to limited number of bits available.

## Slide 10: PIC Architecture Paging / Banking Boundary Summary
PIC16/17
Family
Word
Size
(Bits)
Code
Page
Boundary
(Words)
Current
Max code
Size
(Words)
Register
Bank
Boundary
(Bytes)
Current
Max RAM
Size
(Bytes)
16F5X
12
512
2K
32
73
16FXXX
14
2048
8K
128
368
17CXXX
16
8192
16K/64K
256
902
Notes: Show how each of the cores relates to the different page and bank schemes. Point out that when go thru instruction set the number of bits available for addressing is shown.

## Slide 11: PIC16FXX Architecture Program Memory
Maximum 8K Bytes (13 bits) of program memory space
Four Pages each 2K bytes (11 bits)
Page access using PCLATH<4:3>
Reset Vector at 0000h
Interrupt Vector at 0004h
Page 0
0000h
0004h
07FFh
Interrupt
Reset
Page 1
0800h
0FFFh
Page 2
1000h
17FFh
Page 3
1800h
1FFFh
PCLATH<4:3> = 00
PCLATH<4:3> = 01
PCLATH<4:3> = 10
PCLATH<4:3> = 11
Notes: <number>
<footer>
<header>
<date/time>
Reset vector at 0, Interrupt vector at 4h
In 2K Program memory, PCLATH has no impact
In 4K Program memory, PCLATH bit 3 selects 2K page. Since PCLATH is not ininialized on reset (POR or otherwise), user must initialize PCLATH after reset.

## Slide 12: PIC Architecture Paging program memory
Paging needs consideration ONLY when executing program CALL or GOTO operation
Modify page bits ONLY when jumping to different page than last jumped
  page bits define desired page execution
Instructions invoking page bits:
  GOTO <address>
  CALL <address>
  <Instruction> PCL,F ; e.g. ADDWF PCL,F
There are no paging considerations when returning
Notes: For this slide and next 4, refer to data sheets as needed to clarify and get them use to looking in DS for the different data.
Ask Why the last bullet is true.
Answer: Because the Stack is full width.

## Slide 13: PIC Architecture Paging program memory
ADDWF PCL,F has eight bits (256 words) of address
  In PIC16C5X PA0, PA1 determine final page
    Bit 8 of PC is cleared by hardware
    Destination address must be first 256 of page
  In PIC16CXXX/17CXXX, PCLATH is used for upper address
    Destination address can be anywhere
    Look-up tables that cross a 256 word boundary require pre-conditioning of PCLATH
Notes: 5x is a x12 core tell them how the x12 is acceses pages versus how the 16c/17c acceses the pages.

## Slide 14: PIC Architecture Paging program memory
PC
12
8
7
0
5
PCLATH<4:0>
PCLATH
INST with PCL
as dest
ALU result
GOTO, CALL
Opcode <10:0>
8
PC
12
11
10
0
11
PCLATH<4:3>
PCH
PCL
8
7
2
PCLATH
PCH
PCL
PIC16F84A
PA1:PA0
2
STATUS
PC
8
7
0
PCL
9
10
PA1:PA0
2
STATUS
PC
8
7
0
PCL
9
10
Instruction Word
Reset to ‘0’
Instruction Word
7
0
7
0
GOTO Instruction
CALL or Modify PCL Instruction
PIC16F56
Notes: Tell students that on 12 bit core the page bits are pulled from status.
On 14 bit core the page bits come from pclath.

## Slide 15
PC<12:0>
Stack Level 1



Stack Level 8
Reset Vector
Peripheral Interrupt Vector
User Memory
Space
CALL, RETURN
RETFIE, RETLW
13
0000h
0004h
1FFFh
3FFh
PIC16F58
Program Memory Map
PIC16F84A
PC<10:0>
Stack Level 1
Stack Level 2
User Memory
Space
11
000h
1FFh
Reset Vector
0FFh
100h
On-chip Program
Memory (Page 0)
On-chip Program
Memory (Page 1)
On-chip Program
Memory (Page 2)
On-chip Program
Memory (Page 3)
200h
3FFh
2FFh
300h
400h
5FFh
4FFh
500h
600h
7FFh
6FFh
700h
CALL, RETLW
Notes: 0 to 3ff on The x12 has 1 page boundries on the x14 there arent any page boundries. Why? Because you have 2 more bits.

## Slide 16
PIC Architecture Program Memory: Immediate Operation
  8-bit constant (literal) value included in
    instruction word.
  Used by literal instructions such as
  movlw, addlw, retlw, etc.
OP CODE
k
14-bit Instruction for Literal Instructions
k
k
k
k
k
k
k
Notes: Paging where do I get the extra bits I need

## Slide 17
PIC Architecture Program Memory: PC Absolute Addressing
OP CODE
k
k
k
k
14-bit Instruction for call and goto
k
k
k
k
k
k
k
  Used by control instructions CALL and GOTO
  to modify the PC (Program Counter)
k
k
k
k
k
k
k
k
k
x
x
x
k
k
x
x
x
PCLATH Register
Effective 13-bit Program Memory Address
11-bits From Instruction
2-bits
From
PCLATH
k
k
k
k
Notes: How many bits doesit take to address 8K of Program Memory?

## Slide 18
PIC Architecture PC Relative Addressing (14-bit core)
PCH <5>
PCL <8>
13-Bit Program Counter
PCLATH <5>
Internal Data Bus <8>
5
5
8
  First write high byte to PCLATH.
  Next write low byte to PCL, this loads the entire
13-bit value to PC.
movlw HIGH Delay
movwf PCLATH
movlw LOW Delay
movwf PCL
Note: PCH cannot be read
Notes: Tricky way to get the bits you need to address 8K

## Slide 19
00000000
XXXXXXXX
PIC MCU Architecture PC Relative Addressing
Look-up Table Example
movlw HIGH Decode
movwf PCLATH
movf DisplayValue,W
call Decode
movwf PORTB
goto Continue
Decode
addwf PCL,F
retlw B’00111111’ ;decode 0
retlw B’00000110’ ;decode 1
retlw B’01011011’ ;decode 2
retlw B’01001111’ ;decode 3
retlw B’01100110’ ;decode 4
retlw B’01101101’ ;decode 5
retlw B’01111101’ ;decode 6
retlw B’00000111’ ;decode 7
retlw B’01111111’ ;decode 8
retlw B’01101111’ ;decode 9
Continue
b
e
g
a
f
d
c
RB0
RB1
RB2
RB3
RB4
RB5
RB6
b
c
d
e
f
g
W Register
I/O Port B
01101101
00000101
movf DisplayValue,W
call Decode
addwf PCL,F
retlw B’01101101’ ;decode 5
movwf PORTB
01101101
g
a
f
d
c
b
e

## Slide 20: PIC16FXX Architecture Data Memory
Four banks each of 128 bytes of Data Memory
Special Function Registers (SFRs) are mapped in top 32 locations
Banks selected by RP0,1 and IRP in Status register
GPRs
SFRs
Bank0
000h
01Fh
020h
07Fh
GPRs
SFRs
Bank1
080h
09Fh
0A0h
0FFh
0F0h
GPRs
SFRs
Bank2
100h
11Fh
120h
17Fh
170h
GPRs
SFRs
Bank3
180h
19Fh
1A0h
1FFh
1F0h
RP<1:0> RP<1:0> RP<1:0> RP<1:0>
= 00 = 01 = 10 = 11
Notes: <number>
<footer>
<header>
<date/time>
RP1 and IRP should not be used as GP bits, in order to maintain upward compatibility.
RP0 selects between bank 0 and bank 1.
A “r/w” to bank 2 and 3 will be a “r/w” to bank 0 or 1 depending on the state of RP0.
Explain due to number of bits available banking is a efficient way to get more memory.
Same as program memory limitations in # of bits thus 4 banks.
What are the shaded in yellow and what are they usefull for?

## Slide 21: PIC Architecture Methods for accessing data memory
Direct
Indirect

## Slide 22: PIC Architecture Data Memory: Direct Addressing
7-bit direct address from the instruction
2-bits from STATUS register
Effective 9-bit Register Address
IRP
RP1
RP0
OP CODE
TO
PD
Z
DC
C
STATUS Register
14-bit Instruction
f
f
f
f
f
f
f
RP1
RP0
f
f
f
f
f
f
f
7-bits From Instruction Word
2-bits From
STATUS
Register

## Slide 23: PIC Architecture Data Memory: Indirect Addressing
IRP
f
f
f
f
f
f
f
f
f
8-bit indirect address from the FSR (File Select Register).
1-bit from STATUS register.
IRP
RP1
RP0
TO
PD
Z
DC
C
f
f
f
f
f
f
f
STATUS Register
8-bit FSR Register
Effective 9-bit Register Address
8-bits From FSR
1-bit From
STATUS
Register

## Slide 24: PIC Architecture Data Memory: Indirect Addressing
      Clear all RAM locations from 0x20 to 0x7F.
      Indirect address is loaded into FSR.
      Every time INDF is used as operand, register pointed to by FSR is actually used.
movlw 0x20
movwf FSR
LOOP clrf INDF
incf FSR,F
btfss FSR,7
goto LOOP
<next instruction>
0000 0000
0000 0000
FSR = 20h
INDF
00h
04h
20h
7Fh
Data Memory

## Slide 25: PIC Architecture Data memory map
File Address
00
h
01
h
02
h
03
h
04
h
05
h
06
h
07
h
08
h
09
h
0A
h
0B
h
0C
h
7F
h
80
h
81
h
82
h
83
h
84
h
8
5h
86
h
87
h
88
h
89
h
8A
h
8B
h
8
Ch
FF
h
Bank 0
Bank 1
Indirect addr.
(1)
Indirect addr.
(1)
TMR0
OPTION
_REG
PCL
STATUS
FSR
PORTA
PORTB
EEDATA
EEADR
PCLATH
INTCON
68
General
Purpose
Registers
SRAM)
PCL
STATUS
FSR
TRISA
TRISB
EECON1
EECON2
(1)
PCLATH
INTCON
Mapped
in Bank 0
Unimplemented data memory location; read as '0'.
File Address
Not a physical register.
CFh
D0h
4Fh
50h
(accesses)
Register File Map
PIC16F84A
Notes: Note to students that 508 ds shows no bank 1.

## Slide 26: Quiz 2
1) What bits must you set prior to calling a subroutine?
2) What bits must you set prior to returning from a subroutine?
3) Data tables in program memory do not need to have page bits set.
Both
Page
Bank
Neither
Both
Page
Bank
Neither
True
False
Notes: Let students work on this for 5 min. then review with them like quiz 1.
1)page
2)neither
3)false

## Slide 27: Quiz2 (cont.)
4) For the 12-bit core, what SFR register and respective bits are needed to access different pages in program memory ?
5) For the 14-bit core, what SFR register and respective bits are needed to access different pages in program memory?
6) What bits are needed to access different RAM banks?
___________________________________________________________________________
___________________________________________________________________________
1)________________________2)________________________3)________________________4)________________________
Notes: 4)PA1 & PA0, Opcode itself, PC
5)PCLATH <4:3>, Opcode itself, PCL
6)Direct: RP<1:0>, Opcode itself,
Indirect IRP, FSR