To:	Dr. Hoover

From:	Mark Jacobson, CM #1130

Date:	October 18, 2007

Project Number/Title: Lab 4B: Background Task with Foreground Interrupt Tasks

This interrupt lab was created to instruct the students in how to write interrupt service routines. It also required the student to hardware debounce an spst pushbutton switch and to learn to work with both the input and output compare functions on the microcontroller.

As attachments 1 indicates, the microcontroller was attached to additional support circuitry in order for it to function as desired. Multiple signal LED's were used to indicate both the unlocking of the combination lock and the frequency of the input square wave.

The program flow chart can be found in attachment 3 and was created based on an initial design statement issued by Dr. Hoover. The main program can be found on the first page, with all interrupt routines found on the next page.

Attachment 3 contains the commented assembly code that both enables and then uses the interrupt functionality on the chip in order to accomplish the task.

The program/circuit combination was tested one step at a time to determine that a particular interrupt routine was functional before adding another one.

The final circuit/program combination was shown to be successful by the end of the lab period after some initial delays in enabling the interrupt routines.